## Slide 1: Small Cell Deployment –
What happens when the technology and the real world meet
Chris Stratton FRICS MRTPI
Notes: Good afternoon
Chair of the RICS Expert Working Group on Telecoms and Director of CPS
interested in small cells for over a decade and followed the activities of the Small Cell Forum. I’m interested specifically in outdoor small cells. I’ll explain why they are becoming more important and why this is relevant today
In 2013 SC were the coming thing. I watched Arqiva pay London and other Authorities for concessions, almost always based on using lampposts. At previous company helped one of the mobile operators manage an outdoor Wi-Fi/small cell network across London installed for the Olympics. Worked on a bid to provide small cell solution for another Operator and I got a call from a third Operator, ten minutes after a journalist asked the Chief Exec what his Small Cell Policy was.
Government even supported deployment by granting statutory consent for small cells, through the GPDO – I helped define what a small cell was, for the legislation
So for ten years, solutions have been ready to go. Desire has been there and yet they haven’t happened. Why?

## Slide 2: Outdoor Small Cell Network - BACKGROUND
Location sensitive – Lampposts are not always the answer
Transmission – fibre or radio
Limited Need – 2G & 3G fills 4G & 5G holes
Too hard and too expensive
Concentrate resources on macro layer
Notes: Assumption has always been that small cells can be mounted on lampposts. But, they are highly sensitive, locationally. Is there a lamppost in the right place, or is it round the corner, so half the desired coverage area is in radio shadow. If there is a lamppost, is it capable of supporting the antennas and where does any necessary equipment go? Does it provide sufficient height - What happens when a bus goes past? Is it a Listed Structure?
In the ‘street canyon’, would attaching the antenna to a building be a better solution, from a radio point of view? (That brings in a whole new range of potential issues. Carlos will be talking about some of the ways these are being mitigated, later)
As the lamppost has its own requirement, power will be available, unless, as my old Customer found out, the Christmas light contractors come along and unplug the small cell, in late November, to use the small cell supply. But how to connect the cell into the network? Fibre will require expensive digging but, unless a mesh network is installed – and will work at street level, a radio TX may need a second system; will the lamppost accommodate it?
Current network coverage is provided by multiple technologies, on different frequencies, each with differing footprints, as a result. The lower frequencies of the 2G & 3G networks will provide greater range and penetration than the higher frequencies, generally, used by 4 & 5G, so there were few Not Spots, in overall coverage. Marginal benefits in creating ubiquitous 4 & 5G, when 2 & 3G coverage was sound, were not financially justifiable. Money was restricted to necessary spend, where it was really needed.

## Slide 3: Outdoor Small Cell Network - BACKGROUND
Location sensitive – Lampposts are not always the answer
Transmission – fibre or radio
Limited Need – 2G & 3G fills 4G & 5G holes
Too hard and too expensive
Concentrate resources on macro layer
Notes: Assumption has always been that small cells can be mounted on lampposts. But, they are highly sensitive, locationally. Is there a lamppost in the right place, or is it round the corner, so half the desired coverage area is in radio shadow. If there is a lamppost, is it capable of supporting the antennas and where does any necessary equipment go? Does it provide sufficient height - What happens when a bus goes past? Is it a Listed Structure?
In the ‘street canyon’, would attaching the antenna to a building be a better solution, from a radio point of view? (That brings in a whole new range of potential issues. Carlos will be talking about some of the ways these are being mitigated, later)
As the lamppost has its own requirement, power will be available, unless, as my old Customer found out, the Christmas light contractors come along and unplug the small cell, in late November, to use the small cell supply. But how to connect the cell into the network? Fibre will require expensive digging but, unless a mesh network is installed – and will work at street level, a radio TX may need a second system; will the lamppost accommodate it?
Current network coverage is provided by multiple technologies, on different frequencies, each with differing footprints, as a result. The lower frequencies of the 2G & 3G networks will provide greater range and penetration than the higher frequencies, generally, used by 4 & 5G, so there were few Not Spots, in overall coverage. Marginal benefits in creating ubiquitous 4 & 5G, when 2 & 3G coverage was sound, were not financially justifiable. Money was restricted to necessary spend, where it was really needed.

## Slide 4: Outdoor Small Cell Network - CURRENT
Burgeoning need developing – 2G & 3G sunset horizon
Technology solutions - Small Cells v RAN Extenders
Engineering Problem – Lamppost v Dedicated Mast v Building
Co-operative Site Providers - Local Authorities (Govt Policy & DCIA*)
  - Third Parties (with Code enforcement)
  - Planning permission granted (GPDO)
  Cost - Existing Use Value + Compensation
Notes: So – What’s changed?
Dates for 2G & 3G networks’ sunset is on the horizon, the holes in the 4G & 5G networks will become plainly apparent. The time has come for outdoor small cells as a solution.
Hardware needs to be cheap – avoid the BTS – IS Telecom Soln

## Slide 5: Outdoor Small Cell Network - FUTURE
Telecom Code - Solved some problems but created others
- Upper Lands Tribunal for dispute resolution ADR
- Barrier Busting Workshops:
- Functional Issues
- Template Agreements for Fibre and for Mobile
- Education & Communication
National Connectivity Alliance
Notes: Property side – facilitated by Govt. as much as they can BUT – Code created disengagement with independent site providers. At macro level – negligible income – walked away and resisted Operators attempts to use Code Rights.
Govt. set up Barrier Busting Workshops to address lack of collaboration to try to free up the mechanism for 5G roll-out. Ran for 2.5 years. Covered functional issues, template agreements for mobile and fibre installations and educational/communication.
Committed to telecom infrastructure deployment but not Govt function to take responsibility for delivering industry solutions. Workshop contributors came together to pick up where the workshops left off – National Connectivity Alliance.