## Slide 1
Ericsson 5G market & stadium solutions
Fredrik Tägt
Strategic Product Manager (SPM)
Product Line Indoor Radio
Ericsson HQ Sweden
5G market dynamics and trends
Stadium and arena solutions

## Slide 2: 3 key 5G use case (monetization) enablers
5G enablers
Midband (3.5GHz)*
Stand Alone (SA)
Differentiated connectivity (network slicing ect)
* mmW in US
Use cases

## Slide 3: Globally, 5G mid-band population coverage has reached around 45%
Mid-band population coverage, split by region (end of 2023)
5G band deployment
Global 5G map showing 5G speed test samples per frequency range (Android devices only)
45%, 5G mid-band population coverage has reached around 45% at the end of 2023
310
Global 5G Live Networks (GSA, March 2024)
45%
5G mid - band population coverage by the end of 2023 (Ericsson 2023)
49
Global SA Live Public Networks (GSA, May 2024)
1.6 B
5G subscriptions by the end of 2023 (Ericsson 2023)
Source: Ericsson analysis on Speedtest Intelligence® data from Ookla®. Only android devices Note: Speedtest measurements per 5G frequency band. Samples from the period Jan 1st, 2024 to May30th, 2024.
Commercial in confidence, © Ericsson AB 2024
*Source: Ericsson Mobility Report, June 2024
Chart: 
| World | World (Without China) | North America | Europe (Without Russia) | Latin America | Middle East and Africa | Asia-Pacific (Without India and China) | India | China
5G mid-band | 0.45 | 0.35 | 0.85 | 0.3 | 0.1 | 0.1 | 0.2 | 0.9 | 0.95
5G total | 0.5 | 0.4 | 0.9 | 0.7 | 0.1 | 0.1 | 0.2 | 0.9 | 0.95

## Slide 4
5G NSA vs SA coverage area
Source: Ericsson analysis on Speedtest Intelligence® data from Ookla®. Note: Samples include iOS and Android smartphones connecting to a 5G NSA/SA network. Samples from the period April 2024 to Oct 2024.
Red = 5G NSA
Green = 5G SA
Commercial in confidence, © Ericsson AB 2024
348
Global Live 5G networks
Live 5G SA networks
60+
170
Ericsson Live 5G networks
Ericsson Live 5G SA networks
37

## Slide 5: Enabling monetization Enabling high performing programmable networks
Best effort MBB performance
One-network-fits-all
Today's networks Non-Stand alone (NSA)
Monetization “ready” network Stand Alone (SA)
Midband
“Network Slicing” Service SLA fulfilment
Differentiated connectivity
Programable
APIs
Positioning
Energy efficiency

## Slide 6: CSP use case monetization strategy with differentiated connectivity though slicing
Chart: 
| Year 1 | Year 2 | Year 3 | Year 4 | Year 5 | Year 6
eMBB | 100 | 60 | 30 | 20 | 10 | 10
Revenue without use case (Slicing) Monetization
Revenue
Chart: 
| Year 1 | Year 2 | Year 3 | Year 4 | Year 5 | Year 6
eMBB | 100 | 60 | 30 | 20 | 10 | 0
Economy Slices | 0 | 40 | 70 | 80 | 90 | 100
Premium Slices | 0 | 10 | 18 | 24 | 26 | 28
Enterprise Slices | 0 | 0 | 10 | 18 | 24 | 26
Revenue with use case (Slicing) Monetization
in
partnership
with
Use case 1
Use case 2
Use case 3
Use case 4
Use case 1

## Slide 7: Singtel building up the 5G SA capabilities to support different use cases (slices)
2020
2021
2022
2023
2024
Nationwide 5G SA in Singapore
Monetization with Slicing
  5G network slicing to stream football matches: FIFA World Cup Qatar
Continue to develop new network-slicing
5G Non-Stand Alone (NSA) “Launch”
5G SA Market Trial
5G Stand Alone (SA) “Launch”
1st Ericsson commercial network slice for Formula 1
in
partnership
with
  Pioneer Security as a slice (Secaas)
Slicing
basic slicing enabled
security slice added
event pass slice added

## Slide 8: 5G Stadium use cases Guaranteed performance with “5G Event pass”
Event (‘Express’) Pass – For users who wants best user experience during events

## Slide 9: 5G Stadium use cases Live Sports Broadcasting partnership over 5G SA network
Specifications
Massive MIMO radios
  AIR 3278
  AIR 5322
  Baseband 6648
NR Dual-Connectivity (Stand-alone)
  Max modulation = 256 QAM
Sony PDT-FP1 5G transmitter
  Qualcomm X70 Chipset
Haivision PRO unit
  Video Codec = H.265
First event to use new Sony 5G NR-DC wireless transmitter!
Ericsson, 3 Denmark, TV 2, and Sony kick off live broadcast
TV2, Ericsson, 3 and Sony trial live 5G-mmWave international football transmission - TVBEurope
TDD band n78
TDD band n258
800 MHz
20 MHz

## Slide 10
Mission Critical Services Priority-based connectivity and tailored features
Indoor & Outdoor Positioning Localization-based services with or without GPS assistance
5G
Stadium 5G use case for First responder
Differentiated connectivity Use Cases Enabled by 5G Standalone + slicing
T‑Mobile Introduces ‘T‑Priority’ Featuring the World’s First Network Slice for First Responders
Location server
First responder
central
First responder filed

## Slide 11: Building Stadium 5G Capacity Methodology
Capacity Boost Solutions with 5G massive MIMO

## Slide 12: Advancing 5G network performance Massive MIMO for mmW and Midband (3.5 GHz) and Radio Dot System (RDS)
Coverage
Mid-band TDD
Low-band FDD
High-band
mmW
~30 versions of M-MIMO radios options available for each deployment scenario
Bring Massive MIMO to every site
For extreme high capacity
Basic Coverage Layer
Performance & Bandwidth
5G B78
3,5 GHz
ect
2G/3G/4G B1 2,1 GHz
B3 1,8 GHz ect
Massive MIMO mmW
AIR 6419
64T64R 22kg
192AE
AIR 3265 32T32R 12kg
128AE
Radio Dot
Dot 4454 400 MHz 4T4R
AIR 5322 800MHz
AIR 5343 1600Hz
Indoor AIR 1279 800MHz
5G B257/258/260/etc.

## Slide 13: RAN Infrastructure and Equipment Sharing Sharing alternatives
Shared Radio (MOCN&MORAN as well)
Shared RAN (MORAN & MOCN capable)
IRU 16xx
Shared baseband
Single baseband
Shared HW
Shared HW
Multiple baseband
A
B
C
D
A
B
C
D
IRU 16xx
Indoor Connect
8855
BB & Radio
BB & Radio
BB & Radio
Baseband (Ericsson)
Shared HW
Single-vendor RAN
Multi-vendor RAN
A
B
C
D
Shared HW
A
B
C
D
Dedicated baseband
Multi-vendor over S1/NG
Up to 4 connected BB to RDS radio, 2 BB to any other ERS radio
Dot
Shared and/or operator Dedicated baseband
Dot
Multi-vendor over S1/NG
AAS/RRU
IRU 16xx
Dot
AAS/RRU
Dot Only
2x eCPRI connections maximum
Dot Only
IRU 16xx
Dot
AAS/RRU
2x eCPRI connections maximum
AAS/RRU+Dot
AAS/RRU+Dot
Up to 4 connected BB to RDS, 2 BB to any other ERS radio
All 4 solutions can also be mixed in the same network deployment

## Slide 14: Sports venue / cellular coverage evolution
Basic coverage layer (2G/3G/4G)
Extreme high-capacity layer (5G)
Radio Dot System(RDS)
M-MIMO radio (AAS)
B
2
3
1
High-capacity layer (5G)
Capacity
B
Low
band
1
Mid
band
2
High
band
Coverage
Phenomenal
capacity
3
1
2
Main focus for future proof investments
Traditional solution
mmW M-MIMO radio (AAS)
Passive & active DAS

## Slide 15: Massive MIMO basics- reducing cell to cell interference
Antenna Elements
96 elements illustration
traffic beams
Single user (SU) MIMO :4 layers
Multi-user (MU) MIMO: 1–4 users scheduled on different beams
Beamforming
dBi
High energy
Low energy
Beamforming
M-MIMO radio
Notes: 2x8 array of subarrays

## Slide 16: Why Massive MIMO
Higher capacity  up to 7 times vs traditional solutions
Ease of installation
Less space requirement

## Slide 17: M-MIMO Down Link (DL) Capacity Up to 7 times higher capacity wit same number of sectors
Product | Active DAS | AAS 32TR | 
Deployment | 4x4 SU-MIMO | 4x4 SU-MIMO | MU-MIMO
# Sectors | 11 | 11 | 11
Downlink
Served traffic [GB/h] | 631 | 2007 | 4798
>7 times increase
>3 times increased
11 sectors A-DAS
11 sectors Massive MIMO
SINR
SINR
Baseline

## Slide 18: M-MIMO Up Link (UL) Capacity Up to 5times higher capacity wit same number of sectors
Product | Active DAS | AAS 32TR |  | 
Deployment | SU-MIMO | 1x4 Rx diversity | UL 2x4 SU-MIMO | MU-MIMO
# Sectors | 11 | 11 | 11 | 11
Served traffic [GB/h] (1) | 187 | 299.3 | 532.7 | 939.5
~ 5 times increase
~ 3 times increase
~ 1.5
(1) max served traffic in the entire arena while satisfying a UL throughput of 2 Mbps for 95% of the subscribers
11 sectors Massive MIMO
11 sectors A-DAS
SINR
Baseline
Up link

## Slide 19: M-MIMO mounting options Performance impact
Upper tier on the main stand
Radio mounting options
4x4 DL SU-MIMO
4x4 DL SU-MIMO + MU-MIMO
A) Below roof
B) Behind seating area
Stadium de Toulouse
Performance impact
B) Behind seating area
A) Behind seating area

## Slide 20: Energy Efficiency Massive MIMO 5G vs Traditional Radio
NR TDD + M-MIMO is highly energy efficient with higher gains at higher traffic
Incentivize 5G market adoption to improve performance - by offloading LTE - and energy efficiency
Source: Ericsson Network Benchmarking – European CSP data CW20’2024
LTE 1.8GHz
LTE 2.1GHz
20MHz
20MHz
4T4R Dual Band Radio 4499
Samples in green
5G 3.5GHz
100MHz
VS
Massive MIMO 3239
Samples in orange
Energy Consumption vs Traffic – Live network measurement
Energy Consumption (W)
Traffic(GB)

## Slide 21
Qatar World Cup ’22
Massive MIMO radios & Dots
  5G Mid Band in with M-MIMO radio AIR3227
  5G High Band (mmW) in M-MIMO radio AIR5322
  5G Mid Band in indoor locations using 5G DOT 4474 with Indoor Connect 8855
Centralized basebands in stadiums telecom rooms with Elastic RAN
8 stadiums for hosted World Cup ’22

## Slide 22: US Super Bowl 2024
Verizon utilizing a high number of 5G mmWave radios

## Slide 23
Australia
Melbourne Cricket Ground (MCG)
Known as the MCG, or simply the “G”
100,000+ seating Capacity
Massive MIMO Radio both on Mid-band NR and mmWave
NR3500
mmWave
Massive MIMO radios

## Slide 24: Rapid Indoor portfolio evolution Seamless indoor & outdoor experience
2023
2022
2021
2014
2024+
Platform introduction
2018
2017
2016
2019
2020
Dot 2242
Single band
IRU 8850
Dot 4454
Cloud RAN
5G
launch
2T2R
Dot 4479
Single Operator
5G
launch
Dot 4475
Dot 4474
TDD
Tri-band
Dual-band
Indoor Connect 8855 IRU 1649
Indoor AIR
IRU 164x Indoor Connect 8855
Dot 4455
Dot 4459
Dot 2256
Quad
Band
Indoor Fusion
RDS Positioning
Positioning
SMB
400MHz 4T4R
4x capacity
Dual band
2T2R
Dot 4442
Single & Multi Operator
1
Year anniversary
Notes: 2242 B1 PRA in end of 2014
Trends
Single operator (high performing)
Single operator (small building)
Multi-operator
Neutral host
Cloud indoor

## Slide 25: Ericsson Indoor solutions overview Radio Dot , Indoor Fusion, Indoor Air
Core Network(s)
RAN Compute(s)
Indoor / outdoor Serving area
Indoor Fusion Unit (“All in one box”)
Core NW
Medium/Large sized venues
Small/Medium sized venues
CAT6A
10km, Fiber Dot solution
CAT6A, fiber or hybrid fiber
Fiber
Fiber
Indoor AIR 1279
(mmW)
RF signal source 3rd party base station
Indoor Connect 8855
(Multi-vendor support)
Fiber
Coax
Indoor Radio Unit (IRU)
Dot
Dot
Dot
Dot outdoor enclosure
Outdoor
Ericsson Indoor Planner (EIP)
Single - to Quad-band Dot options
Single- and Multi-operator support